## Slide 1: 3 Modeled Systems
Overhead Canopy System
Canal (variable width)
18° Tilt
Single Bank Vertical Bifacial System
Double Bank Vertical Bifacial System
We want to compare PV generation and the irradiance on the water
~5m tall
Array length varies with chosen canal width
Canal (variable width)
Canal (variable width)

## Slide 2: Current Approach (Generation)
Canopy and Single Bank Vertical Bifacial are both single row systems.
Self-shading is disabled, and Ground Coverage Ratio set to minimum value (0.01) for maximum row spacing.
Double Bank Vertical Bifacial
Enable self shading and set GCR to achieve desired real row spacing (Array length / GCR).

## Slide 3: Current Approach (Irradiance on Water)
“Look at output for “Spatial Irradiance incident on the ground between rows (W/m2)”
- SAM divides rows into 10 equally sized boxes.
GCR chosen so box edges line up with canal edges.
Only boxes corresponding to water are kept, while others are discarded.
Relevant boxes averaged to find avg irradiance on water and compared to weather GHI to measure shading impact.
Attempt to keep box size close to overhang distance so the first box can be thrown out.
-> Row spacing stays the same while GCR and array length vary with canal width.
Similar Approach for Single Bank Vertical Bifacial System
For Double Bank Vertical Bifacial , can set to actual row spacing

## Slide 4: The Problem
Even when a system is specified to have only 1 or 2 rows, SAM appears to treat these as interior rows to a larger multi-row system.
This results in unwanted ground shading from these “phantom rows”.
Low angle rays that would strike the first few boxes under the array are blocked by phantom rows.
Phantom rows block ground reflection to vertical panels.

## Slide 5: Possible Solutions
1. Change an internal flag in SAM to treat rows as singular (or first and last in case of Double Bank Vertical).
-BifacialVF has a parameter for “Rowtype” that can be set to first, interior, last, or single. Does SAM have a similar internal variable that can be changed?
2. Instead of dividing row spacing into 10 boxes, can it be changed to 100 or any arbitrarily large number?
If so, GCR can be set low so that spacing is high enough for shading impacts to be negligible while maintaining desired box sizes, and we can simply use only the first few boxes.
Will still have problems with Double Bank Vertical Bifacial generation, as spacing is fixed to canal width. May need to decompose that system into several vertical monofacial systems.

## Slide 6: Are these solutions viable? If so, how does one make these internal changes? Are there any other solutions to achieve these modeling goals?